## Slide 1: RAIL: Resilient Analog Instance Language/Library

## Slide 2
Contents
0. RAIL-Lib
1. Design Procedure
2. ADC Architecture
3. Sub-Circuit Design
4. ADC Core Layout
5. Full-Chip ADC Layout

## Slide 3
0. RAIL-Lib
RAIL-Lib is a process-portable standard cell library for mixed signal circuit agile design.
It contains 29 types of 51 standard cells.
1

## Slide 4
Why RAIL-lib?
Short design cycle
You can design and simulation a ADC from schematic to full-chip GDS in 2 weeks.
Open source
You can add and amend standard cells according to your need.
Flexibility
Using RAIL-Lib, you can build operational amplifier, biasing circuit, bootstrap switch, comparator, capacitive DAC array and many other circuits can be used in mixed signal circuits.
No need for custom layout design
You can generate layout using existing TCL scripts by run them in ICC, just need to adjust parameter or exchange standard cell. You can also add and amend these scripts.
Easy to amend your design
You can exchange standard cell in your circuit, without adjustment of W/L of MOSFETs. You can amend your layout by just change TCL script, no need to adjust layout of the whole chip.
0. RAIL-Lib
2

## Slide 5
1. Design Procedure
ADC architecture
Digital logic design & simulation
Analog circuit design & simulation using RAIL-Lib
ADC simulation
ADC simulation
ADC layout & simulation
Full-chip simulation & layout
Analog circuit layout & simulation using RAIL-Lib
Full-chip GDS
Verilog, VDHL or digital standard cell.
Using RAIL-Lib build analog circuits, like bootstrapped switch, comparator et al. Pre-layout simulation.
Using RAIL-Lib build layout of analog circuits, and then post-layout simulation of these analog circuits
Pre-layout simulation of the whole ADC.
Simulation of the whole ADC, pre-layout of digital and post-layout of analog.
Post-layout simulation of the whole ADC.
3

## Slide 6
2. ADC Architecture
Fig. 1. Schematic of the SAR ADC
This is a single channel single stage successive approximation (SAR) ADC. It requires two switches, one comparator, one capacitive DAC (CDAC) array, one voltage controlled delay line (VCDL) used in digital control logic and digital control logic. The switch, comparator, CDAC and VCDL can be designed using RAIL-Lib, which will be elaborated in detail in next chapter.
Switch
Comparator
CDAC
VCDL
4

## Slide 7
3. Sub-Circuit Design
Bootstrap Switch
Fig. 2. schematic of bootstrap switch
Bootstrap switch consists of NSW、PSW、CDC、and CKND
5

## Slide 8
Netlist : src/btsw100m.v
Script : script/btsw100.tcl
Fig. 3. netlist of bootstrap switch
Fig. 4. layout script of bootstrap switch
Set working path
Configure library files path
Placement and routing
Create layout
3. Sub-Circuit Design
Bootstrap Switch
6

## Slide 9
MOM capacitor uses the parasitic capacitance of finger metal in the same layer. The layout script of crt_mom in schematic is as follows:
Fig. 5. layout script of crt_mom in schematic
3. Sub-Circuit Design
Bootstrap Switch
7

## Slide 10
Fig. 6. layout of bootstrap switch
3. Sub-Circuit Design
Bootstrap Switch
8

## Slide 11
Comparator
Comparator consists mainly of Dynamic Pre-amplifier and Latch.
Two VCDC2s in parallel and VCDP2s speeding up discharge compose the Dynamic Pre-Amplifier.
Two MSNR3 in back-to-back connection compose the Latch.
PCAPs therein are used to calibrate offset of comparator
Fig. 7. schematic of comparator
3. Sub-Circuit Design
9

## Slide 12
Comparator
Fig. 8. netlist of comparator
Netlist : src/comp.v
Script : script/comp.tcl
Fig. 9. layout script of comparator
3. Sub-Circuit Design
10

## Slide 13
Comparator
Fig. 10. layout of comparator
3. Sub-Circuit Design
11

## Slide 14
CDAC Array
Using Binary Capacitor Array from Cunit to 256Cunit .
Value of redundant capacitor is 64Cunit .
Using split capacitor in the position of 128Cunit and 256Cunit .
MOM1 is used as unit capacitor.
Fig. 11. schematic of capacitor array
3. Sub-Circuit Design
12

## Slide 15
Fig. 12. netlist of capacitor array
Netlist : src/cdac11b_h.v
3. Sub-Circuit Design
CDAC Array
13

## Slide 16
Script: script/cadc11b_h.tcl
Fig. 13. layout script of capacitor array
3. Sub-Circuit Design
CDAC Array
14

## Slide 17
Fig. 14. layout of MOM1 cell
Fig. 15. layout of capacitor array
3. Sub-Circuit Design
CDAC Array
15

## Slide 18
VCDL
Using VCDC2 and INVD1 chain structure to construct voltage control delay line (VCDL) . Delay decreases with the increasement of control voltage. Schematic is as follows and layout is generate by ICC through automatic placement and routing in digital logic part.
Fig. 16. schematic of VCDL
3. Sub-Circuit Design
16

## Slide 19
ADC core simulation for function verification: replacing switches, comparator, CDAC and VCDL by their corresponding PEX files.
Generate netlist of ADC schematic.
Call the ADC netlist and library files in script.
Create floorplan in ICC.
Placement and routing.
Checking LVS and DRC.
Parasitic parameter extraction.
Post-layout simulation of ADC core.
The whole layout can be generated by TCL script.
4. ADC Core Layout
18

## Slide 20
Fig. 17. Setting library files and configuration files for ADC core
Fig. 18. Calling ADC core netlist
4. ADC Core Layout
18

## Slide 21
4. ADC Core Layout
Fig. 19. Layout of ADC core
19

## Slide 22
Full-chip ADC simulation: using ADC core (post- layout) and pads (pre-layout), verifying the function.
generate netlist of the full-chip ADC.
Call the ADC netlist and library files in script.
Create floorplan in ICC.
Placement and routing.
Checking LVS and DRC.
It should be noticed that, PRES and PRES2 cell in RAIL lib were used to solve problem of DRC. In schematic, these resistors should be replaced by rppoly in tsmcN65 lib.
Fig. 20. Schematic of the full-chip ADC
5. Full-Chip ADC Layout
20

## Slide 23
Fig. 21. Setting library files and configuration files for full-chip ADC
Fig. 22. Calling full-chip ADC netlist
5. Full-Chip ADC Layout
21

## Slide 24
5. Full-Chip ADC Layout
(a)
(b)
(c)
Fig. 24. PRES resistors in full-chip ADC layout: (a) one resistor, (b) 2 resistors shunt, (c) 20 resistors shunt.
Using PRES and PRES2, we can create any small value of resistance (the maximum resistance is about 20Ω).
We should place PRES at two sideways, and PRES2 at middle.
Fig. 23. Layout of PRES (a) and PRES2 (b)
(a) PRES
(b) PRES2
22